## Slide 1
REVOLUTE 2026 · FABLAB KENDALL · PHYSICAL AI / COOKING
YesChef
"Hey chef, make me a sandwich" — then it actually does.
Voice-controlled sandwich assembly on a reBot arm: natural-language orders (including "no tomato / hold the cheese"), vision checks of what's on the table, and soft-ingredient stacking with a compliant TPU gripper.
01 CREATIVITY
The canonical hard joke — built for real
Sandwich assembly = NL understanding + perception + soft-object manipulation. Customizable orders in plain English; stack order preserved exactly as spoken.
02 EDIBILITY
Real food, real station
Bread, tomato, cucumber, cheese, lettuce. Custom containers stage each item predictably. Compliant gripper conforms instead of crushing. Goal: somewhat edible, every run.
03 CHEF'S TAKE
Product, not a lab toy
Guest walks up -> speaks -> robot serves. Kill-switch ladder: full auto -> vision report-only -> trajectory playback -> live teleop so the deli never goes down.
Judging · Product / Taste 30 pts (Creativity · Edibility · Chef's opinion)

## Slide 2
TECHNICAL DIFFICULTY · 30 pts
On-device Physical AI — free models, real motors
1
Wake + STT
Hey chef Whisper tiny.en (local, free)
2
Intent
Qwen2.5 3B Ollama · Jetson sandwich?
3
Parse order
Text matcher preserves sequence not LLM reorder
4
Vision gate
Qwen2.5-VL 3B label-aware check what's present
5
Assemble
Per-ingredient trajectories bread -> stack
AMBITION 10
• Full voice -> vision -> motion loop on Jetson + reBot B601-RS
• SocketCAN + leader teleop + 60 Hz skill library
• 3D-printed compliant TPU gripper for soft food
• Zero paid APIs — Whisper + Ollama CUDA on-device
ACCURACY 10
• Order-preserving ingredient parser (sequence matters)
• Vision prefers text labels over visual guesses
• Per-item trajectories: bread, tomato, cheese, cucumber, lettuce
• Custom containers -> consistent grasp presentation
CONSISTENCY 10
• Hardware fixes: unwrap patch, wrist stops, gripper scale
• VRAM: unload text model before VL; merged vision call
• Trajectory tuning until layers land without drops
• Teleop fallback if any stage flakes

## Slide 3
DOCUMENTATION · 40 pts + LIVE STORY
What we ship for judges — and why it works
DOCUMENTATION COMPLETENESS
10 pts
GitHub
Versioned code + website-style README, voice_agent/, trajectories/, commands.txt runbook
15 pts
Live demo
Science-fair table: speak order -> vision beat -> stack -> Order up! + teleop handoff
10 pts
Demo video
1-min hero + gallery slots in video/ for Devpost / Hackster
5 pts
PPT deck
This deck — solution narrative mapped to the scoring rubric
PROUD OF
• End-to-end voice -> sandwich by the deadline
• Layers landing cleanly — no drops after grasp tuning
• All free / self-hosted models (no cloud STT bill)
• Hardware honesty: unwrap patch, stops, VRAM unload
SCORE MAP · 100 pts
40 Documentation · 30 Technical (ambition / accuracy / consistency) · 30 Product & Taste (creativity / edibility / chef)
WHAT'S NEXT
Dynamic ingredient localization · layer-success feedback · learned policies beyond fixed trajectories · same voice->perception->manipulation loop for any assembly task.